## Slide 1: CS 5600 Computer Systems
Lecture 7: Virtual Memory

## Slide 2
Motivation and Goals
Base and Bounds
Segmentation
Page Tables
TLB
Multi-level Page Tables
Swap Space

## Slide 3: Main Memory
Main memory is conceptually very simple
  Code sits in memory
  Data is either on a stack or a heap
  Everything gets accessed via pointers
  Data can be written to or read from long term storage
Memory is a simple and obvious device
  So why is memory management one of the most complex features in modern OSes?

## Slide 4: Protection and Isolation
Physical memory does not offer protection or isolation
0x00000000
0xFFFFFFFF
Kernel Memory
Process 1
w/ Secret Data
Physical Memory
Evil Process
I’m in your process, stealing your data ;)
Oh sorry, I didn’t mean to overwrite your task_structs ;)

## Slide 5: Compilation and Program Loading
Compiled programs include fixed pointer addresses
Example:
000FE4D8 <foo>:
…
000FE21A: push eax
000FE21D: push ebx
000FE21F: call 0x000FE4D8
Problem: what if the program is not loaded at corresponding address?
0x00000000
0xFFFFFFFF
Kernel Memory
Process 1
Physical Memory
Process 2
Addr of foo(): 0x000FE4D8
Addr of foo(): 0x0DEB49A3

## Slide 6: Physical Memory has Limited Size
RAM is cheap, but not as cheap as solid state or cloud storage
What happens when you run out of RAM?
0x00000000
0xFFFFFFFF
Kernel Memory
Process 1
Process 2
Process 3
Process 4
Process 5

## Slide 7: Physical vs. Virtual Memory
Clearly, physical memory has limitations
  No protection or isolation
  Fixed pointer addresses
  Limited size
  Etc.
Virtualization can solve these problems!
  As well as enable additional, cool features

## Slide 8: A Toy Example
What do we mean by virtual memory?
  Processes use virtual (or logical) addresses
  Virtual addresses are translated to physical addresses
0x0000
0xFFFF
Kernel Memory
Process 1
Physical Memory
(Reality)
Process’ View of
Virtual Memory
0x0000
0xFFFF
Process 2
Process 3
Process 1
All the memory belongs to me!
I am master of all I survey!
Physical Address
Virtual Address
Magical Address Translation Black Box

## Slide 9: Implementing Address Translation
In a system with virtual memory, each memory access must be translated
Can the OS perform address translation?
  Only if programs are interpreted
Modern systems have hardware support that facilitates address translation
  Implemented in the Memory Management Unit (MMU) of the CPU
  Cooperates with the OS to translate virtual addresses into physical addresses

## Slide 10: Virtual Memory Implementations
There are many ways to implement an MMU
  Base and bound registers
  Segmentation
  Page tables
  Multi-level page tables
We will discuss each of these approaches
  How does it work?
  What features does it offer?
  What are the limitations?
Old, simple, limited functionality
Modern, complex, lots of functionality

## Slide 11: Goals of Virtual Memory
Transparency
  Processes are unaware of virtualization
Protection and isolation
Flexible memory placement
  OS should be able to move things around in memory
Shared memory and memory mapped files
  Efficient interprocess communication
  Shared code segments, i.e. dynamic libraries
Dynamic memory allocation
  Grow heaps and stacks on demand, no need to pre-allocate large blocks of empty memory
Support for sparse address spaces
Demand-based paging
  Create the illusion of near-infinite memory

## Slide 12
Motivation and Goals
Base and Bounds
Segmentation
Page Tables
TLB
Multi-level Page Tables
Swap Space

## Slide 13: Base and Bounds Registers
A simple mechanism for address translation
Maps a contiguous virtual address region to a contiguous physical address region
0x0000
0xFFFF
Kernel Memory
Process 1
Physical Memory
0x00FF
0x10FF
Process 1
Process’ View of
Virtual Memory
0x0001
0x1001
Register | Value
EIP | 0x0023
ESP | 0x0F76
BASE | 0x00FF
BOUND | 0x1000

## Slide 14: Base and Bounds Example
0x0000
0xFFFF
Kernel Memory
Process 1
Physical Memory
0x00FF
0x10FF
Process 1
Process’ View of
Virtual Memory
0x0001
0x1001
Register | Value
EIP | 0x0023
ESP | 0x0F76
BASE | 0x00FF
BOUND | 0x1000
0x0023 mov eax, [esp]
1) Fetch instruction
0x0023 + 0x00FF = 0x0122
2) Translate memory access
0x0F76 + 0x00FF = 0x1075
3) Move value to register
[0x1075]  eax
1
2
1
2

## Slide 15: Protection and Isolation
0x0000
0xFFFF
Kernel Memory
Process 1
Physical Memory
0x00FF
0x10FF
Process 1
Process’ View of
Virtual Memory
0x0001
0x1001
Register | Value
EIP | 0x0023
ESP | 0x0F76
BASE | 0x00FF
BOUND | 0x1000
0x0023 mov eax, [0x4234]
1) Fetch instruction
0x0023 + 0x00FF = 0x0122
2) Translate memory access
0x4234 + 0x00FF = 0x4333
0x1333 > 0x10FF
(BASE + BOUND)
Raise Protection Exception!
1
2
1
2

## Slide 16: Implementation Details
BASE and BOUND are protected registers
  Only code in Ring 0 may modify BASE and BOUND
  Prevents processes from modifying their own sandbox
Each CPU has one BASE and one BOUND register
  Just like ESP, EIP, EAX, etc…
  Thus, BASE and BOUND must be saved a restored during context switching

## Slide 17: Base and Bound Pseudocode
PhysAddr = VirtualAddress + BASE
if (PhysAddr >= BASE + BOUND)
RaiseException(PROTECTION_FAULT)
Register = AccessMemory(PhysAddr)

## Slide 18: Advantages of Base and Bound
Simple hardware implementation
Simple to manage each process’ virtual space
Processes can be loaded at arbitrary fixed addresses
Offers protection and isolation
Offers flexible placement of data in memory
0x00000000
0xFFFFFFFF
Kernel Memory
Process 1
Physical Memory
Process 2
I’m loaded at address 0x00AF
No, I’m loaded at address 0x00AF
Previous BASE  0x00FF
New BASE  0x10A0

## Slide 19: Limitations of Base and Bound
Processes can overwrite their own code
  Processes aren’t protected from themselves
No sharing of memory
  Code (read-only) is mixed in with data (read/write)
Process memory cannot grow dynamically
  May lead to internal fragmentation
0x00000000
0xFFFFFFFF
Kernel Memory
/bin/bash
Physical Memory
/bin/bash
Code
Code
Data
Data
Code is duplicated in memory :(

## Slide 20: Internal Fragmentation
BOUND determines the max amount of memory available to a process
How much memory do we allocate?
  Empty space leads to internal fragmentation
What if we don’t allocate enough?
  Increasing BOUND after the process is running doesn’t help
Physical Memory
Code
Heap
Stack
Wasted space = internal fragmentation
Heap
Stack
Increasing BOUND doesn’t move the stack away from the heap

## Slide 21
Motivation and Goals
Base and Bounds
Segmentation
Page Tables
TLB
Multi-level Page Tables
Swap Space

## Slide 22: Towards Segmented Memory
Having a single BASE and a single BOUND means code, stack, and heap are all in one memory region
  Leads to internal fragmentation
  Prevents dynamically growing the stack and heap
Segmentation is a generalization of the base and bounds approach
  Give each process several pairs of base/bounds
    May or may not be stored in dedicated registers
  Each pair defines a segment
  Each segment can be moved or resized independently

## Slide 23: Segmentation Details
The code and data of a process get split into several segments
  3 segments is common: code, heap, and stack
  Some architectures support >3 segments per process
Each process views its segments as a contiguous region of memory
  But in physical memory, the segments can be placed in arbitrary locations
Question: given a virtual address, how does the CPU determine which segment is being addressed?

## Slide 24: Segments and Offsets
Key idea: split virtual addresses into a segment index and an offset
Example: suppose we have 14-bit addresses
  Top 2 bits are the segment
  Bottom 12 bits are the offset
4 possible segments per process
  00, 01, 10, 11
13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Segment
Offset

## Slide 25: Separation of Responsibility
The OS manages segments and their indexes
  Creates segments for new processes in free physical memory
  Builds a table mapping segments indexes to base addresses and bounds
  Swaps out the tables and segment registers during context switches
  Frees segments from physical memory
The CPU translates virtual addresses to physical addresses on demand
  Uses the segment registers/segment tables built by the OS

## Slide 26: Segmentation Example
0x0000
0x3FFF
Process’ View of
Virtual Memory
Code
Segment | Index | Base | Bound
CS (Code) | 00 | 0x0020 | 0x0100
HS (Heap) | 01 | 0xB000 | 0x0100
SS (Stack) | 10 | 0x0400 | 0x0100
0x0023 mov eax, [esp]
1) Fetch instruction
0x0023 (EIP) - 00000000100011
0x0020 (CS) + 0x0023 = 0x0043
2) Translate memory access
0x2015 (ESP) – 10000000010101
0x0400 (SS) + 0x0015 = 0x0415
0x1000
0x0000
0xFFFF
Kernel Memory
Physical Memory
Code
Heap
Stack
Code
Heap
Stack
0x0020
0xB100
0xB000
0x0120
0x0400
0x0500
0x2000
0x3000
Heap
Stack

## Slide 27: Segmentation Pseudocode
// get top 2 bits of 14-bit VA
Segment = (VirtualAddress & SEG_MASK) >> SEG_SHIFT
// now get offset
Offset = VirtualAddress & OFFSET_MASK
if (Offset >= Bounds[Segment])
RaiseException(PROTECTION_FAULT)
else
PhysAddr = Base[Segment] + Offset
Register = AccessMemory(PhysAddr)

## Slide 28: More on Segments
In the previous example, we use a 14-bit address space with 2 bits reserved for the segment index
  This limits us to 4 segments per process
  Each segment is 212 = 4KB in size
Real segmentation systems tend to have
  More bits for the segments index (16-bits for x86)
  More bits for the offset (16-bits for x86)
However, segments are course-grained
  Limited number of segments per process (typically ~4)

## Slide 29: Segment Permissions
Many CPUs (including x86) support permissions on segments
  Read, write, and executable
Disallowed operations trigger an exception
  E.g. Trying to write to the code segment
0x0000
0x3FFF
Process 1’s View of
Virtual Memory
Code
Index | Base | Bound | Permissions
00 | 0x0020 | 0x0100 | RX
01 | 0xB000 | 0x0100 | RW
10 | 0x0400 | 0x0100 | RW
11 | 0xE500 | 0x100 | R
0x1000
0x2000
0x3000
Heap
Stack
.rodata

## Slide 30: x86 Segments
Intel 80286 introduced segmented memory
  CS – code segment register
  SS – stack segment register
  DS – data segment register
  ES, FS, GS – extra segment registers
In 16-bit (real mode) x86 assembly, segment:offset notation is common
  mov [ds:eax], 42 // move 42 to the data segment, offset // by the value in eax
  mov [esp], 23 // uses the SS segment by default

## Slide 31: x86 Segments Today
Segment registers and their associated functionality still exist in today’s x86 CPUs
However, the 80386 introduced page tables
  Modern OSes “disable” segmentation
  The Linux kernel sets up four segments during bootup
Segment Name | Description | Base | Bound | Ring
KERNEL_CS | Kernel code | 0 | 4 GB | 0
KERNEL_DS | Kernel data | 0 | 4 GB | 0
USER_CS | User code | 0 | 4 GB | 3
USER_DS | User data | 0 | 4 GB | 3
Pages are used to virtualize memory, not segments
Used to label pages with protection levels

## Slide 32: What is a Segmentation Fault?
If you try to read/write memory outside a segment assigned to your process
Examples:
  char buf[5];
  strcpy(buf, “Hello World”);
  return 0; // why does it seg fault when you return?
Today “segmentation fault” is an anachronism
  All modern systems use page tables, not segments

## Slide 33: Shared Memory
0x0000
0x3FFF
Process 1’s View of
Virtual Memory
Code
Index | Base | Bound
00 | 0x0020 | 0x0100
01 | 0xB000 | 0x0100
10 | 0x0400 | 0x0100
11 | 0xE500 | 0x0300
0x1000
0x2000
0x3000
Heap
Stack
0x0000
0x3FFF
Process 2’s View of
Virtual Memory
0x1000
0x2000
0x3000
Code
Heap
Stack
Shared Data
Shared Data
Index | Base | Bound
00 | 0x0020 | 0x0100
01 | 0xC000 | 0x0100
10 | 0x0600 | 0x0100
11 | 0xE500 | 0x0300
Same 00 and 01 physical segments
Different 01 and 10 physical segments

## Slide 34: Advantages of Segmentation
All the advantages of base and bound
Better support for sparse address spaces
  Code, heap, and stack are in separate segments
  Segment sizes are variable
  Prevents internal fragmentation
Supports shared memory
Per segment permissions
  Prevents overwriting code, or executing data

## Slide 35: External Fragmentation
Problem: variable size segments can lead to external fragmentation
  Memory gets broken into random size, non-contiguous pieces
Example: there is enough free memory to start a new process
  But the memory is fragmented :(
Compaction can fix the problem
  But it is extremely expensive
Kernel Memory
Physical Memory
Code
Heap
Stack
Code
Heap
Stack
Heap
Stack
Code
Code
Heap
Stack
Code
Heap
Stack

## Slide 36
Motivation and Goals
Base and Bounds
Segmentation
Page Tables
TLB
Multi-level Page Tables
Swap Space

## Slide 37: Towards Paged Memory
Segments improve on base and bound, but they still aren’t granular enough
  Segments lead to external fragmentation
The paged memory model is a generalization of the segmented memory model
  Physical memory is divided up into physical pages (a.k.a. frames) of fixed sizes
  Code and data exist in virtual pages
  A table maps virtual pages  physical pages (frames)

## Slide 38: Toy Example
Suppose we have a 64-byte virtual address space
  Lets specify 16 bytes per page
How many bits do virtual addresses need to be in this system?
  26 = 64 bytes, thus 6 bit addresses
Page 0
0
64
16
32
48
Page 1
Page 2
Page 3
Virtual Memory
How many bits of the virtual address are needed to select the physical page?
  64 bytes / 16 bytes per page = 4 pages
  22 = 4, thus 2 bits to select the page
5 | 4 | 3 | 2 | 1 | 0
Virtual Page #
Offset

## Slide 39: Toy Example, Continued
Page 0
0
64
16
32
48
Page 1
Page 2
Page 3
Virtual Memory
Page 0
0
64
16
32
48
Page 1
Page 2
Page 3
Physical Memory
Page 4
128
96
112
Page 5
Page 6
Page 7
80
Virtual Page # | Physical Page #
00 (0) | 010 (2)
01 (1) | 111 (7)
10 (2) | 100 (4)
11 (3) | 001 (1)
mov eax, [21]
Translation
21 – 010101
117 – 1110101

## Slide 40: Concrete Example
Assume a 32-bit virtual and physical address space
  Fix the page size at 4KB (4096 bytes, 212)
How many total pages will there be?
  232 / 212 = 1048576 (220)
How many bits of a virtual address are needed to select the physical page?
  20 bits (since there are 1048576 total pages)
Assume that each page table entry is 4 bytes large
  How big will the page table be?
  1048586 * 4 bytes = 4MB of space
Each process needs its own page table
100 processes = 400MB of page tables

## Slide 41: Concrete Example, Continued
Process 1 requires:
  2 KB for code (1 page)
  7 KB for stack (2 pages)
  12 KB for heap (3 pages)
0
232
Process 1’s View of
Virtual Memory
Code
Heap
Stack
Heap
Heap
Stack
VPN | PFN | Valid?
0 … i - 1 | whatever | 0
i | d | 1
i + 1 … j – 1 | whatever | 0
j | b | 1
j + 1 | f | 1
j + 2 | e | 1
j + 3 … k - 1 | whatever | 0
k | a | 1
k + 1 | c | 1
Page i
Page j
Page j + 1
Page j + 2
Page k
Page k + 1
0
230
Kernel Memory
Physical Memory
Code
Heap
Stack
Heap
Heap
Stack
Page a
Page b
Page c
Page d
Page e
Page f
The vast majority of each process’ page table is empty, i.e. the table is sparse
Heap
Heap
Page j + 3
Page g
Modify [ j+3, g, 1]

## Slide 42: Page Table Implementation
The OS creates the page table for each process
  Page tables are typically stored in kernel memory
  OS stores a pointer to the page table in a special register in the CPU (CR3 register in x86)
  On context switch, the OS swaps the pointer for the old processes table for the new processes table
The CPU uses the page table to translate virtual addresses into physical addresses

## Slide 43: x86 Page Table Entry
On x86, page table entries (PTE) are 4 bytes
31 - 12 | 11 - 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Page Frame Number (PFN) | Unused | G | PAT | D | A | PCD | PWT | U/S | W | P
Bits related to permissions
  W – writable bit – is the page writable, or read-only?
  U/S – user/supervisor bit – can user-mode processes access this page?
Hardware caching related bits: G, PAT, PCD, PWT
Bits related to swapping
  P – present bit – is this page in physical memory?
  A – accessed bit – has this page been read recently?
  D – dirty bit – has this page been written recently?
We will revisit these later in the lecture…

## Slide 44: Page Table Pseudocode
// Extract the VPN from the virtual address
VPN = (VirtualAddress & VPN_MASK) >> SHIFT
// Form the address of the page-table entry (PTE)
PTEAddr = PTBR + (VPN * sizeof(PTE))
// Fetch the PTE
PTE = AccessMemory(PTEAddr)
if (PTE.Valid == False) // Check if process can access the page
RaiseException(SEGMENTATION_FAULT)
else if (CanAccess(PTE.ProtectBits) == False)
RaiseException(PROTECTION_FAULT)
// Access is OK: form physical address and fetch it
offset = VirtualAddress & OFFSET_MASK
PhysAddr = (PTE.PFN << PFN_SHIFT) | offset
Register = AccessMemory(PhysAddr)

## Slide 45: Tricks With Permissions and Shared Pages
Recall how fork() is implemented
  OS creates a copy of all pages controlled by the parent
fork() is a slooooow operation
  Copying all that memory takes a looooong time
Can we improve the efficiency of fork()?
  Yes, if we are clever with shared pages and permissions!

## Slide 46: Copy-on-Write
Key idea: rather than copy all of the parents pages, create a new page table for the child that maps to all of the parents pages
  Mark all of the pages as read-only
  If parent or child writes to a page, a protection exception will be triggered
  The OS catches the exception, makes a copy of the target page, then restarts the write operation
Thus, all unmodified data is shared
  Only pages that are written to get copied, on demand

## Slide 47: Copy-on-Write Example
0
230
Kernel Memory
Physical Memory
Code
Heap
Stack
Page a
Page d
Page f
Function | VPN | PFN | Writable?
Code | i | d | 0
Heap | j | b | 1
Stack | k | a | 1
Parents Page Table
Function | VPN | PFN | Writable?
Code | i | d | 0
Heap | j | b | 0
Stack | k | a | 0
Childs Page Table
0
0
Protection Exception
Stack
Page m
1
1
Stack
m
Write
Write
Write

## Slide 48: Zero-on-Reference
How much physical memory do we need to allocate for the heap of a new process?
  Zero bytes!
When a process touches the heap
  Segmentation fault into OS kernel
  Kernel allocates some memory
  Zeros the memory
    Avoid accidentally leaking information!
  Restart the process

## Slide 49: Advantages of Page Tables
All the advantages of segmentation
Even better support for sparse address spaces
  Each page is relatively small
  Fine-grained page allocations to each process
  Prevents internal fragmentation
All pages are the same size
  Each to keep track of free memory (say, with a bitmap)
  Prevents external fragmentation
Per segment permissions
  Prevents overwriting code, or executing data

## Slide 50: Problems With Page Tables
Page tables are huge
  On a 32-bit machine with 4KB pages, each process’ table is 4MB
  One a 64-bit machine with 4KB pages, there are 240 entries per table  240 * 4 bytes = 4TB
  And the vast majority of entries are empty/invalid!
Page table indirection adds significant overhead to all memory accesses

## Slide 51: Page Tables are Slow
0x1024 mov [edi + eax * 4], 0x0
0x1028 inc eax
0x102C cmp eax, 0x03E8
0x1030 jne 0x1024
How many memory accesses occur during each iteration of the loop?
  4 instructions are read from memory
  [edi + eax * 4] writes to one location in memory
  5 page table lookups
    Each memory access must be translated
    … and the page tables themselves are in memory
Naïve page table implementation doubles memory access overhead

## Slide 52
Motivation and Goals
Base and Bounds
Segmentation
Page Tables
TLB
Multi-level Page Tables
Swap Space

## Slide 53: Problem: Page Table Speed
Page tables give us a great deal of flexibility and granularity to implement virtual memory
However, page tables are large, thus they must go in RAM (as opposed to in a CPU register)
  Each virtual memory access must be translated
  Each translation requires a table lookup in memory
  Thus, memory overhead is doubled
How can we use page tables without this memory lookup overhead?

## Slide 54: Caching
Key idea: cache page table entries directly in the CPU’s MMU
  Translation Lookaside Buffer (TLB)
  Should be called address translation cache
TLB stores recently used PTEs
  Subsequent requests for the same virtual page can be filled from the TLB cache
Directly addresses speed issue of page tables
  On-die CPU cache is very, very fast
  Translations that hit the TLB don’t need to be looked up from the page table in memory

## Slide 55: Example TLB Entry
VPN & PFN – virtual and physical pages
G – is this page global (i.e. accessible by all processes)?
ASID – address space ID
  D – dirty bit – has this page been written recently?
  V – valid bit – is this entry in the TLB valid?
  C – cache coherency bits – for multi-core systems
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
ASID
G
Virtual Page Number (VPN)
V
D
C
Physical Frame Number (PFN)
More on this later…

## Slide 56: TLB Control Flow Psuedocode
VPN = (VirtualAddress & VPN_MASK) >> SHIFT
(Success, TlbEntry) = TLB_Lookup(VPN)
if (Success == True) // TLB Hit
if (CanAccess(TlbEntry.ProtectBits) == True)
Offset = VirtualAddress & OFFSET_MASK
PhysAddr = (TlbEntry.PFN << SHIFT) | Offset
AccessMemory(PhysAddr)
else
RaiseException(PROTECTION_FAULT)
else // TLB Miss
PTEAddr = PTBR + (VPN * sizeof(PTE))
PTE = AccessMemory(PTEAddr)
if (PTE.Valid == False)
RaiseException(SEGMENTATION_FAULT)
else if (CanAccess(PTE.ProtectBits) == False)
RaiseException(PROTECTION_FAULT)
TLB_Insert(VPN, PTE.PFN, PTE.ProtectBits)
RetryInstruction()
Load the page table entry from memory, add it to the TLB, and retry
Make sure we have permission, then proceed
Fast Path
Slow Path

## Slide 57: Reading an Array (no TLB)
Suppose we have a 10KB array of integers
  Assume 4KB pages
With no TLB, how many memory accesses are required to read the whole array?
  10KB / 4 = 2560 integers in the array
  Each requires one page table lookup, one memory read
  5120 reads, plus more for the instructions themselves

## Slide 58: Reading an Array (with TLB)
Same example, now with TLB
  10KB integer array
  4KB pages
  Assume the TLB starts off cold (i.e. empty)
How many memory accesses to read the array?
  2560 to read the integers
  3 page table lookups
  2563 total reads
  TLB hit rate: 96%
Process 1’s View of
Virtual Memory
Array Data
Array Data
Array Data
Page j
Page j + 1
Page j + 2
VPN | PFN
j | a
j + 1 | b
j + 2 | c
TLB

## Slide 59: Locality
TLB, like any cache, is effective because of locality
  Spatial locality: if you access memory address x, it is likely you will access x + 1 soon
    Most of the time, x and x + 1 are in the same page
  Temporal locality: if you access memory address x, it is likely you will access x again soon
    The page containing x will still be in the TLB, hopefully

## Slide 60: Be Careful With Caching
Recall: TLB entries have an ASID (address space ID) field. What is this for?
  Here’s a hint: think about context switching
VPN | PFN
i | d
j | b
k | a
Process 1’s Page Table
VPN | PFN
i | r
j | u
k | s
Process 2 Page Table
VPN | PFN
i | d
J | b
k | a
TLB
VPNs are the same, but PFN mappings have changed!
Problem: TLB entries may not be valid after a context switch

## Slide 61: Potential Solutions
Clear the TLB (mark all entries as invalid) after each context switch
  Works, but forces each process to start with a cold cache
  Only solution on x86 (until ~2008)
Associate an ASID (address space ID) with each process
  ASID is just like a process ID in the kernel
  CPU can compare the ASID of the active process to the ASID stored in each TLB entry
  If they don’t match, the TLB entry is invalid

## Slide 62: Replacement Policies
On many CPUs (like x86), the TLB is managed by the hardware
Problem: space in the TLB is limited (usually KB)
  Once the TLB fills up, how does the CPU decide what entries to replace (evict)?
Typical replacement policies:
  FIFO: easy to implement, but certain access patterns result in worst-case TLB hit rates
  Random: easy to implement, fair, but suboptimal hit rates
  LRU (Least Recently Used): algorithm typically used in practice

## Slide 63: Hardware vs. Software Management
Thus far, discussion has focused on hardware managed TLBs (e.g. x86)
  PTE = AccessMemory(PTEAddr)
  TLB_Insert(VPN, PTE.PFN, PTE.ProtectBits)
  CPU dictates the page table format, reads page table entries from memory
  CPU manages all TLB entries
However, software managed TLBs are also possible (e.g. MIPS and SPARC)

## Slide 64: Software Managed TLB Pseudocode
VPN = (VirtualAddress & VPN_MASK) >> SHIFT
(Success, TlbEntry) = TLB_Lookup(VPN)
if (Success == True) // TLB Hit
if (CanAccess(TlbEntry.ProtectBits) == True)
Offset = VirtualAddress & OFFSET_MASK
PhysAddr = (TlbEntry.PFN << SHIFT) | Offset
Register = AccessMemory(PhysAddr)
else
RaiseException(PROTECTION_FAULT)
else // TLB Miss
RaiseException(TLB_MISS)
The hardware does not:
Try to read the page table
Add/remove entries from the TLB

## Slide 65: Implementing Software TLBs
Key differences vs. hardware managed TLBs
  CPU doesn’t insert entries into the TLB
  CPU has no ability to read page tables from memory
On TLB miss, the OS must handle the exception
  Locate the correct page table entry in memory
  Insert the PTE into the TLB (evict if necessary)
  Tell the CPU to retry the previous instruction
Note: TLB management instructions are privileged
  Only the kernel can modify the TLB

## Slide 66: Comparing Hardware and Software TLBs
Hardware TLB
Advantages
  Less work for kernel developers, CPU does a lot of work for you
Disadvantages
  Page table data structure format must conform to hardware specification
  Limited ability to modify the CPUs TLB replacement policies
Software TLB
Advantages
  No predefined data structure for the page table
  OS is free to implement novel TLB replacement policies
Disadvantages
  More work for kernel developers
  Beware infinite TLB misses!
    OSes page fault handler must always be present in the TLB
Greater flexibility
Easier to program

## Slide 67: TLB Summary
TLBs address the slowdown associated with page tables
  Frequently used page table entries are cached in the CPU
  Prevents repeated lookups for PTEs in main memory
Reduce the speed overhead of page tables by an order of magnitude or more
  Caching works very well in this particular scenario
  Lots of spatial and temporal locality

## Slide 68
Motivation and Goals
Base and Bounds
Segmentation
Page Tables
TLB
Multi-level Page Tables
Swap Space

## Slide 69: Problem: Page Table Size
At this point, we have solved the TLB speed issue
However, recall that pages tables are large and sparse
  Example: 32-bit system with 4KB pages
  Each page table is 4MB
  Most entries are invalid, i.e. the space is wasted
How can we reduce the size of the page tables?
  Many possible solutions
  Multi-layer page tables are most common (x86)

## Slide 70: Simple Solution: Bigger Pages
Suppose we increase the size of pages
  Example: 32-bit system, 4MB pages
  232 / 222 = 1024 pages per process
  1024 * 4 bytes per page = 4KB page tables
What is the drawback?
  Increased internal fragmentation
  How many programs actually have 4MB of code, 4MB of stack, and 4MB of heap data?

## Slide 71: Alternate Data Structures
Thus far, we’ve assumed linear page tables
  i.e. an array of page table entries
What if we switch to an alternate data structure?
  Hash table
  Red-black tree
Why is switching data structures not always feasible?
  Can be done of the TLB is software managed
  If the TLB is hardware managed, then the OS must use the page table format specified by the CPU

## Slide 72: Inverted Page Tables
Our current discussion focuses on tables that map virtual pages to physical pages
What if we flip the table: map physical pages to virtual pages?
  Since there is only one physical memory, we only need one inverted page table!
VPN | PFN
i | d
j | b
k | a
VPN | PFN
i | r
j | u
k | s
VPN | PFN
i | r
j | u
k | s
PFN | VPN
i | d
j | b
k | a
Standard page tables: one per process
Inverted page tables: one per system
Traditional Tables
Inverted Table

## Slide 73: Normal vs. Inverted Page Tables
Advantage of inverted page table
  Only one table for the whole system
Disadvantages
  Lookups are more computationally expensive
  How to implement shared memory?
VPN | PFN
i | d
j | b
k | a
PFN | VPN
i | d
j | b
k | a
VPN serves as an index into the array, thus O(1) lookup time
Traditional Table
Inverted Table
Table must be scanned to locate a given VPN, thus O(n) lookup time

## Slide 74: Multi-Level Page Tables
Key idea: split the linear page table into a tree of sub-tables
  Benefit: branches of the tree that are empty (i.e. do not contain valid pages) can be pruned
Multi-level page tables are a space/time tradeoff
  Pruning reduces the size of the table (saves space)
  But, now the tree must be traversed to translate virtual addresses (increased access time)
Technique used by modern x86 CPUs
  32-bit: two-level tables
  64-bit: four-level tables

## Slide 75: Multi-Level Table Toy Example
Imagine a small, 16KB address space
  64-byte pages, 14-bit virtual addresses, 8 bits for the VPN and 6 for the offset
How many entries does a linear page table need?
  28 = 256 entries
0
214
Process 1’s View of
Virtual Memory
Stack
Heap
Code
Page 0
Page 4
Page 255
Assume 3 pages out of 256 total pages are in use

## Slide 76: From Linear to Two-levels Tables
How do you turn a linear table into a multi-level table?
  Break the linear table up into page-size units
256 table entries, each is 4 bytes large
  256 * 4 bytes = 1KB linear page tables
Given 64-byte pages, a 1KB linear table can be divided into 16 64-byte tables
  Each sub-table holds 16 page table entries
13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Virtual Page #
Offset
Page Directory Index
(Table Level 1)
Page Table Index
(Table Level 2)

## Slide 77
VPN | PFN | Valid?
00000000 | a | 1
... |  | 0
00000100 | b | 1
… |  | 0
11111111 | c | 1
Linear Page Table
0
214
Process 1’s View of
Virtual Memory
Stack
Heap
Code
Page 0
Page 4
Page 255
13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Offset
Virtual Page Number
253 tables entries are empty, space is wasted :(

## Slide 78
0
214
Process 1’s View of
Virtual Memory
Stack
Heap
Code
Page 0
Page 4
Page 255
13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Offset
Page Directory
Index
Page Table
Index
Index | PFN | Valid?
0000 | a | 1
… |  | 0
0100 | b | 1
… |  | 0
Page Table 0000
Index | PFN | Valid?
0000 |  | 0
… |  | 0
1111 | c | 1
Page Table 1111
Index | Valid?
0000 | 1
0001 | 0
0010 | 0
… | 0
1111 | 1
Page Directory
Empty sub-tables don’t need to be allocated :)

## Slide 79: 32-bit x86 Two-Level Page Tables
31
24
23
16
15
8
7
0
10-bits
PD Index
10-bits
PT Index
12-bits
Offset
Physical
Memory
CR3
Register
Page
Directory
Page
Tables

## Slide 80: 64-bit x86 Four-Level Page Tables
31
24
23
16
15
8
7
0
9-bits
PD1
Index
9-bits
PT Index
12-bits
Offset
Physical
Memory
CR3
Register
Page
Directory 3
Page
Directories 2
63
56
55
48
47
40
39
32
9-bits
PD2
Index
9-bits
PD3
Index
Page
Directories 1
Page
Tables

## Slide 81: Don’t Forget the TLB
Multi-level pages look complicated
  And they are, but only when you have to traverse them
The TLB still stores VPN  PFN mappings
  TLB hits avoid reading/traversing the tables at all

## Slide 82: Multi-Level Page Table Summary
Reasonably effective technique for shrinking the size of page tables
  Implemented by x86
Canonical example of a space/time tradeoff
  Traversing many levels of table indirection is slower than using the VPN as an index into a linear table
  But, linear tables waste a lot of space

## Slide 83
Motivation and Goals
Base and Bounds
Segmentation
Page Tables
TLB
Multi-level Page Tables
Swap Space

## Slide 84: Status Check
At this point, we have a full-featured virtual memory system
  Transparent, supports protection and isolation
  Fast (via TLBs)
  Space efficient (via multi-level tables)
Are we done?
  No!
What if we completely run out of physical memory?
  Can virtualization help?

## Slide 85: Swap Space
Key idea: take frames from physical memory and swap (write) them to disk
  This frees up space for other code and data
Load data from swap back into memory on-demand
  If a process attempts to access a page that has been swapped out…
  A page-fault occurs and the instruction pauses
  The OS can swap the frame back in, insert it into the page table, and restart the instruction

## Slide 86: Swapping Example
Suppose memory is full
The user opens a new program
Swap out idle pages to disk
If the idle pages are accessed, page them back in
0x0000
0xFFFF
Kernel Memory
Process 1
Process 2
Process 3
Process 4
Process 5
Active
Active
Active
Idle
Hard
Drive

## Slide 87: All Modern OSes Support Swapping
On Linux, you create a swap partition along with your normal ext3/4 filesystem
  Swapped pages are stored in this separate partition
Windows

## Slide 88: Implementing Swap
Data structures are needed to track the mapping between pages in memory and pages on disk
Meta-data about memory pages must be kept
  When should pages be evicted (swapped to disk)?
  How do you choose which page to evict?
The functionality of the OSes page fault handler must be modified

## Slide 89: x86 Page Table Entry, Again
On x86, page table entries (PTE) are 4 bytes
31 - 12 | 11 - 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Page Frame Number (PFN) | Unused | G | PAT | D | A | PCD | PWT | U/S | W | P
P – present bit – is this page in physical memory?
  OS sets or clears the present bit based on its swapping decisions
    1 means the page is in physical memory
    0 means the page is valid, but has been swapped to disk
  Attempts to access an invalid page or a page that isn’t present trigger a page fault

## Slide 90: Handling Page Faults
Thus far, we have viewed page faults as bugs
  i.e. when a process tries to access an invalid pointer
  The OS kills the process that generate page faults
However, now handling page faults is more complicated
  If the PTE is invalid, the OS still kills the process
  If the PTE is valid, but present = 0, then
    The OS swaps the page back into memory
    The OS updates the PTE
    The OS instructs the CPU to retry the last instruction

## Slide 91: Page Fault Pseudocode
VPN = (VirtualAddress & VPN_MASK) >> SHIFT
(Success, TlbEntry) = TLB_Lookup(VPN)
if (Success == True) // TLB Hit
if (CanAccess(TlbEntry.ProtectBits) == True)
Offset = VirtualAddress & OFFSET_MASK
PhysAddr = (TlbEntry.PFN << SHIFT) | Offset
Register = AccessMemory(PhysAddr)
else RaiseException(PROTECTION_FAULT)
else // TLB Miss
PTEAddr = PTBR + (VPN * sizeof(PTE))
PTE = AccessMemory(PTEAddr)
if (PTE.Valid == False) RaiseException(SEGMENTATION_FAULT)
if (CanAccess(PTE.ProtectBits) == False)
RaiseException(PROTECTION_FAULT)
if (PTE.Present == True) // assuming hardware-managed TLB
TLB_Insert(VPN, PTE.PFN, PTE.ProtectBits)
RetryInstruction()
else if (PTE.Present == False) RaiseException(PAGE_FAULT)

## Slide 92: When Should the OS Evict Pages?
Memory is finite, so when should pages be swapped?
On-demand approach
  If a page needs to be created and no free pages exist, swap a page to disk
Proactive approach
  Most OSes try to maintain a small pool of free pages
  Implement a high watermark
  Once physical memory utilization crosses the high watermark, a background process starts swapping out pages

## Slide 93: What Pages Should be Evicted?
Known as the page-replacement policy
What is the optimal eviction strategy?
  Evict the page that will be accessed furthest in the future
  Provably results in the maximum cache hit rate
  Unfortunately, impossible to implement in practice
Practical strategies for selecting which page to swap to disk
  FIFO
  Random
  LRU (Least recently used)
Same fundamental algorithms as in TLB eviction

## Slide 94: Examples of Optimal and LRU
Optimal (Furthest in the Future)
Access | Hit/Miss? | Evict | Cache State
0 | Miss |  | 0
1 | Miss |  | 0, 1
2 | Miss |  | 0, 1, 2
0 | Hit |  | 0, 1, 2
1 | Hit |  | 0, 1, 2
3 | Miss | 2 | 0, 1, 3
0 | Hit |  | 0, 1, 3
3 | Hit |  | 0, 1, 3
1 | Hit |  | 0, 1, 3
2 | Miss | 3 | 0, 1, 2
0 | Hit |  | 0, 1, 2
LRU
Access | Hit/Miss? | Evict | Cache State
0 | Miss |  | 0
1 | Miss |  | 0, 1
2 | Miss |  | 0, 1, 2
0 | Hit |  | 0, 1, 2
1 | Hit |  | 0, 1, 2
3 | Miss | 2 | 0, 1, 3
0 | Hit |  | 0, 1, 3
3 | Hit |  | 0, 1, 3
1 | Hit |  | 0, 1, 3
2 | Miss | 0 | 1, 2, 3
0 | Miss | 3 | 0, 1, 2
Assume the cache can store 3 pages

## Slide 95
When memory accesses are random, its impossible to be smart about caching
All memory accesses are to 100% random pages

## Slide 96
LRU does a better job of keeping “hot” pages in RAM than FIFO or random
80% of memory accesses are for 20% of pages

## Slide 97
The process sequentially accesses one memory address in 50 pages, then loops
When the cache size is C < 50, LRU evicts page X when page X + C is read
Thus, pages are not in the cache during the next iteration of the loop
When C >= 50, all pages are cached, thus hit rate = 100%

## Slide 98: Implementing Historical Algorithms
LRU has high cache hit rates in most cases…
… but how do we know which pages have been recently used?
Strategy 1: record each access to the page table
  Problem: adds additional overhead to page table lookups
Strategy 2: approximate LRU with help from the hardware

## Slide 99: x86 Page Table Entry, Again
On x86, page table entries (PTE) are 4 bytes
31 - 12 | 11 - 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Page Frame Number (PFN) | Unused | G | PAT | D | A | PCD | PWT | U/S | W | P
Bits related to swapping
  A – accessed bit – has this page been read recently?
  D – dirty bit – has this page been written recently?
  The MMU sets the accessed bit when it reads a PTE
  The MMU sets the dirty bit when it writes to the page referenced in the PTE
  The OS may clear these flags as it wishes

## Slide 100: Approximating LRU
The accessed and dirty bits tell us which pages have been recently accessed
But, LRU is still difficult to implement
  On eviction, LRU needs to scan all PTEs to determine which have not been used
  But there are millions of PTEs!
Is there a clever way to approximate LRU without scanning all PTEs?
  Yes!

## Slide 101: The Clock Algorithm
Imagine that all PTEs are arranged in a circular list
The clock hand points to some PTE P in the list
  function clock_algo() {
  start = P;
  do {
  if (P.accessed == 0) {
  evict(P);
  return;
  }
  P.accessed = 0;
  P = P.next;
  } while (P != start);
  evict_random_page();
  }

## Slide 102: Incorporating the Dirty Bit
More modern page eviction algorithms also take the dirty bit into account
For example: suppose you must evict a page, and all pages have been accessed
  Some pages are read-only (like code)
  Some pages have been written too (i.e. they are dirty)
Evict the non-dirty pages first
  In some cases, you don’t have to swap them to disk!
  Example: code is already on the disk, simply reload it
Dirty pages must always be written to disk
  Thus, they are more expensive to swap

## Slide 103: RAM as a Cache
RAM can be viewed as a high-speed cache for your large-but-slow spinning disk storage
  You have GB of programs and data
  Only a subset can fit in RAM at any given time
Ideally, you want the most important things to be resident in the cache (RAM)
  Code/data that become less important can be evicted back to the disk