## Slide 1: CS 4700 / CS 5700 Network Fundamentals
Lecture 9: Intra Domain Routing
Revised 7/30/13

## Slide 2: Network Layer, Control Plane
Function:
  Set up routes within a single network
Key challenges:
  Distributing and updating routes
  Convergence time
  Avoiding loops
Application
Presentation
Session
Transport
Network
Data Link
Physical
BGP
RIP
OSPF
Control Plane
Data Plane

## Slide 3: Internet Routing
Internet organized as a two level hierarchy
First level – autonomous systems (AS’s)
  AS – region of network under a single administrative domain
  Examples: Comcast, AT&T, Verizon, Sprint, etc.
AS’s use intra-domain routing protocols internally
  Distance Vector, e.g., Routing Information Protocol (RIP)
  Link State, e.g., Open Shortest Path First (OSPF)
Connections between AS’s use inter-domain routing protocols
  Border Gateway Routing (BGP)
  De facto standard today, BGP-4

## Slide 4: AS Example
AS-1
AS-2
AS-3
Interior Routers
BGP Routers

## Slide 5: Why Do We Need ASs?
Routing algorithms are not efficient enough to execute on the entire Internet topology
Different organizations may use different routing policies
Allows organizations to hide their internal network structure
Allows organizations to choose how to route across each other (BGP)
Easier to compute routes
Greater flexibility
More autonomy/independence

## Slide 6: Routing on a Graph
Goal: determine a “good” path through the network from source to destination
What is a good path?
  Usually means the shortest path
  Load balanced
  Lowest $$$ cost
Network modeled as a graph
  Routers  nodes
  Link  edges
    Edge cost: delay, congestion level, etc.
A
B
C
D
E
F
5
2
3
5
2
1
1
2
3
1

## Slide 7: Routing Problems
Assume
  A network with N nodes
  Each node only knows
    Its immediate neighbors
    The cost to reach each neighbor
How does each node learn the shortest path to every other node?
A
B
C
D
E
F
5
2
3
5
2
1
1
2
3
1

## Slide 8: Intra-domain Routing Protocols
Distance vector
  Routing Information Protocol (RIP), based on Bellman-Ford
  Routers periodically exchange reachability information with neighbors
Link state
  Open Shortest Path First (OSPF), based on Dijkstra
  Each network periodically floods immediate reachability information to all other routers
  Per router local computation to determine full routes

## Slide 9: Outline
Distance Vector Routing
  RIP
Link State Routing
  OSPF
  IS-IS

## Slide 10: Distance Vector Routing
What is a distance vector?
  Current best known cost to reach a destination
Idea: exchange vectors among neighbors to learn about lowest cost paths
Routing Information Protocol (RIP)
Destination | Cost
A | 7
B | 1
D | 2
E | 5
F | 1
DV Table
at Node C
No entry for C
Initially, only has info for immediate neighbors
  Other destinations cost = ∞
Eventually, vector is filled

## Slide 11: Distance Vector Routing Algorithm
Wait for change in local link cost or message from neighbor
Recompute distance table
If least cost path to any destination has changed, notify neighbors

## Slide 12: Distance Vector Initialization
Dest. | Cost | Next
B | 2 | B
C | 7 | C
D | ∞ | 
2
3
1
A
B
C
D
1
7
Node A
Dest. | Cost | Next
A | 2 | A
C | 1 | C
D | 3 | D
Node B
Dest. | Cost | Next
A | 7 | A
B | 1 | B
D | 1 | D
Node C
Dest. | Cost | Next
A | ∞ | 
B | 3 | B
C | 1 | C
Node D
Initialization:
for all neighbors V do
if V adjacent to A
D(A, V) = c(A,V);
else
D(A, V) = ∞;
…

## Slide 13: Distance Vector: 1st Iteration
Dest. | Cost | Next
B | 2 | B
C | 7 | C
D | ∞ | 
2
3
1
A
B
C
D
1
7
Node A
Dest. | Cost | Next
A | 2 | A
C | 1 | C
D | 3 | D
Node B
Dest. | Cost | Next
A | 7 | A
B | 1 | B
D | 1 | D
Node C
Dest. | Cost | Next
A | ∞ | 
B | 3 | B
C | 1 | C
Node D
…
loop:
…
else if (update D(V, Y) received from V)
for all destinations Y do
if (destination Y through V)
D(A,Y) = D(A,V) + D(V, Y);
else
D(A, Y) =
min(D(A, Y),
D(A, V) + D(V, Y));
if (there is a new min. for dest. Y)
send D(A, Y) to all neighbors
forever
8
C
D(A,D) = min(D(A,D), D(A,C)+D(C,D))
= min(∞, 7 + 1) = 8
3
B
5
B
D(A,C) = min(D(A,C), D(A,B)+D(B,C))
= min(7, 2 + 1) = 3
D(A,D) = min(D(A,D), D(A,B)+D(B,D))
= min(8, 2 + 3) = 5
2
C
4
B
3
B

## Slide 14: Distance Vector: End of 3rd Iteration
Dest. | Cost | Next
B | 2 | B
C | 3 | B
D | 4 | B
2
3
1
A
B
C
D
1
7
Node A
Dest. | Cost | Next
A | 2 | A
C | 1 | C
D | 2 | C
Node B
Dest. | Cost | Next
A | 3 | B
B | 1 | B
D | 1 | D
Node C
Dest. | Cost | Next
A | 4 | C
B | 2 | C
C | 1 | C
Node D
…
loop:
…
else if (update D(V, Y) received from V)
for all destinations Y do
if (destination Y through V)
D(A,Y) = D(A,V) + D(V, Y);
else
D(A, Y) =
min(D(A, Y),
D(A, V) + D(V, Y));
if (there is a new min. for dest. Y)
send D(A, Y) to all neighbors
forever
Nothing changes, algorithm terminates
Until something changes…

## Slide 15
4
1
A
B
C
50
loop:
wait (link cost update or update message)
if (c(A,V) changes by d)
for all destinations Y through V do
D(A,Y) = D(A,Y) + d
else if (update D(V, Y) received from V)
for all destinations Y do
if (destination Y through V)
D(A,Y) = D(A,V) + D(V, Y);
else
D(A, Y) = min(D(A, Y), D(A, V) + D(V, Y));
if (there is a new minimum for destination Y)
send D(A, Y) to all neighbors
forever
1
Node B
Node C
Time
D | C | N
A | 4 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 1 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 1 | A
C | 1 | B
D | C | N
A | 2 | B
B | 1 | B
D | C | N
A | 1 | A
C | 1 | B
D | C | N
A | 2 | B
B | 1 | B
Link Cost Changes,
Algorithm Starts
Algorithm Terminates
Good news travels fast
Notes: Change circles to rectangles, don’t block the text

## Slide 16: Count to Infinity Problem
4
1
A
B
C
50
60
Node B
Node C
Time
D | C | N
A | 4 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 6 | C
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 6 | C
C | 1 | B
D | C | N
A | 7 | B
B | 1 | B
D | C | N
A | 8 | C
C | 1 | B
D | C | N
A | 7 | B
B | 1 | B
Node B knows D(C, A) = 5
However, B does not know the path is C  B  A
Thus, D(B,A) = 6 !
Bad news travels slowly

## Slide 17: Poisoned Reverse
4
1
A
B
C
50
60
Node B
Node C
Time
D | C | N
A | 4 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 60 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 60 | A
C | 1 | B
D | C | N
A | 50 | A
B | 1 | B
D | C | N
A | 51 | C
C | 1 | B
D | C | N
A | 50 | A
B | 1 | B
If C routes through B to get to A
  C tells B that D(C, A) = ∞
  Thus, B won’t route to A via C
Does this completely solve this count to infinity problem?
NO
Multipath loops can still trigger the issue

## Slide 18: Outline
Distance Vector Routing
  RIP
Link State Routing
  OSPF
  IS-IS

## Slide 19: Link State Routing
Each node knows its connectivity and cost to direct neighbors
Each node tells every other node this information
Each node learns complete network topology
Use Dijkstra to compute shortest paths

## Slide 20: Flooding Details
Each node periodically generates Link State Packet
  ID of node generating the LSP
  List of direct neighbors and costs
  Sequence number (64-bit, assumed to never wrap)
  Time to live
Flood is reliable (ack + retransmission)
Sequence number “versions” each LSP
Receivers flood LSPs to their own neighbors
  Except whoever originated the LSP
LSPs also generated when link states change

## Slide 21: Dijkstra’s Algorithm
Step | Start S | B | C | D | E | F
0 | A | 2, A | 5, A | 1, A | ∞ | ∞
1 | AD |  | 4, D |  | 2, D | ∞
2 | ADE |  | 3, E |  |  | 4, E
3 | ADEB |  |  |  |  | 
4 | ADEBC |  |  |  |  | 
5 | ADEBCF |  |  |  |  | 
A
B
C
D
E
F
5
2
3
5
2
1
1
2
3
1
Initialization:
S = {A};
for all nodes v
if v adjacent to A
then D(v) = c(A,v);
else D(v) = ∞;
…
…
Loop
find w not in S s.t. D(w) is a minimum;
add w to S;
update D(v) for all v adjacent
  to w and not in S:
D(v) = min( D(v), D(w) + c(w,v) );
until all nodes in S;

## Slide 22: OSPF vs. IS-IS
Favored by companies, datacenters
More optional features
Built on top of IPv4
  LSAs are sent via IPv4
  OSPFv3 needed for IPv6
Favored by ISPs
Less “chatty”
  Less network overhead
  Supports more devices
Not tied to IP
  Works with IPv4 or IPv6
OSPF
IS-IS
Two different implementations of link-state routing

## Slide 23: Different Organizational Structure
OSPF
IS-IS
Area 0
Area 1
Area 2
Area 3
Area 4
Organized around overlapping areas
Area 0 is the core network
Organized as a 2-level hierarchy
Level 2 is the backbone
Level 2
Level 1
Level 1-2

## Slide 24: Link State vs. Distance Vector
 | Link State | Distance Vector
Message Complexity | O(n2*e) | O(d*n*k)
Time Complexity | O(n*log n) | O(n)
Convergence Time | O(1) | O(k)
Robustness | Nodes may advertise incorrect link costs Each node computes their own table | Nodes may advertise incorrect path cost Errors propagate due to sharing of DV tables
n = number of nodes in the graph
d = degree of a given node
k = number of rounds
Which is best?
In practice, it depends.
In general, link state is more popular.

## Slide 25: Outline
Distance Vector Routing
  RIP
Link State Routing
  OSPF
  IS-IS

## Slide 26: OSPF Performance
OSPF processing has practical implications
  Impacts route convergence
  (In)stability of the network
Bulk of OSPF processing is due to LSAs
  Uses network resources (e.g. duplicate LSAs are bad)
  Triggers Dijkstra, consumes CPU
Models predict problems with OSPF processing
  Example: synchronization
Question: what is the behavior of OSPF in reality?

## Slide 27: Enterprise Network Case Study
OSPF network
  15 areas, 500 routers
    This case study covers 8 areas, 250 routers
    One month: April 2002
  Databases and applications live in area 0
  Link-layer = Ethernet-based LANs
Customers are connected via leased lines
  Customer routes are injected via EIGRP into OSPF
    The routes are propagated via external LSAs
    Quite reasonable for the enterprise network in question

## Slide 28: Measurement Architecture
Area 1
Area 0
Area 2
LSAR 1
LSAR 2
LSAG
Real-time Monitoring
OSPFScan
Offline Analysis
Customer Routes
Customer Routes
Reflectors
Listen to LSA advertisements
Do not advertise new routes

## Slide 29: Categorizing LSA Traffic
Refresh LSA
  Periodic refresh of router soft-state (30 minute timer)
  Forms baseline of LSA traffic
  Question: does it synchronize, as predicted?
Change LSA
  Triggered by changes in link state
  May indicate an anomaly or problem
Duplicate LSA
  Reliable flooding may results in duplicate LSAs
  Wastes resources, should be minimized

## Slide 30: LSA Traffic in Different Areas
Area 4
Days
Area 3
Days
Area 2
Days
Area 0
Days
Duplicate
LSAs
Change
LSAs
Refresh
LSAs
Why so many dups?
Why so many changes?
Why so many changes?
30
In theory, all regions are supposed to be homogeneous
Why is there so much variation?

## Slide 31: Refresh LSAs
Refresh LSA traffic is predictable
  Derived from configuration file information
  Important for workload modeling
Area 2
Area 3
Days
Days

## Slide 32: Refresh is Not Synchronized
No evidence of synchronization
  Contrary to simulation-based study
Reasons
  Changes in the topology help break synchronization
  Drift in the refresh interval of different routers
32
No clumping of LSAs

## Slide 33: Causes of Change LSAs
Persistent problems lead to numerous change LSAs
  Internal LSA spikes due to hardware router problems
    Identified a problem early and led to preventive maintenance
  External LSA spikes due to customer route volatility
    Overload of an external link causes EIGRP session on that link to flap
33
Bizarre, temporal problems

## Slide 34: Overhead from Duplicate LSAs
Why do some areas witness substantial duplicate LSA traffic?
  Control plane asymmetry during LSA flooding
  Some announcement patterns results in significant duplicates
Days
34

## Slide 35: Summary of Results
Challenge assumptions about LSA synchronization
  Refresh LSAs are bulk of traffic
  Models predict synchronization
  In practice, this problem doesn’t occur
Detect, diagnose, and act on anomalies
  Existing, SNMP based measures are inadequate
  Change LSAs indicate partial failure modes
    Essentially, an early warning system before total failure
Propose changes to improve performance
  Simple configuration changes to reduce duplicate LSAs